## Slide 1: Chapter 2 – Data Extraction for Resource Conservation
Notes: Estimated time for this lecture: 1 hr
Section(s) omitted in this PPT file –
2.3 - Data extraction for mass exchange processes

## Slide 2: Introduction
Data extraction – most crucial step for any resource conservation activity
Once the data is wrongly extracted, we might end up synthesising a sub-optimum resource conservation network (RCN).
Limiting data needed for process sinks and sources:
  Quantity aspect – flowrate
  Quality aspects:
    Mass integration-based RCN – impurity concentration
    Property integration – linearised operator for property mixing rule

## Slide 3: Segregation for material sources

## Slide 4: Heuristic 1
Keep material sources segregated to maximise their recovery potential.

## Slide 5: Ex 2.1 – Water minimisation in Acrylonitrile (AN) production
Reactor
Decanter
Distillation Column
O2
Aqueous layer
Scrubber
NH3
C3H6
Steam-jet Ejector
Steam
Wastewater to Biotreatment
Off-Gas Condensate
Condensate
Bottoms
Water
AN to sales
6.0 kg H2O/s
5.0 kg AN/s
5.1 kg H2O/s
+ Gases
Tail gases to disposal
Boiler
BFW
1.2 kg H2O/s
14 ppm NH3
0.4 kg AN/s
4.6 kg H2O/s
18 ppm NH3
4.6 kg AN/s
6.5 kg H2O/s
10 ppm NH3
4.2 kg AN/s
1.0 kg H2O/s
25 ppm NH3
0.4 kg AN/s
5.5 kg H2O/s
0 ppm NH3
0.1 kg AN/s
0.7 kg H2O/s
1 ppm NH3
3.9 kg AN/s
0.3 kg H2O/s
34 ppm NH3
0.2 kg AN/s
1.2 kg H2O/s
20 ppm NH3
1.1 kg AN/s
12.0 kg H2O/s

## Slide 6: Ex 2.1 – Process description
AN is produced in a fluidised-bed reactor (2 atm & 450ºC) via vapour-phase ammoxidation of propylene.
The reaction is single-pass, with almost complete conversion of propylene, with following stoichiometry
Effluent from the reactor is cooled and partially condensed. The off-gas from the condenser is sent to a scrubber for purification; while its condensate to the biotreatment facility.

## Slide 7: Ex 2.1 – Process description
Fresh water is used as the scrubbing agent in the scrubber, before the tail gas may be sent for disposal.
The bottom product from the scrubber is sent to a decanter when it is separated into aqueous (sent to the biotreatment facility) & organic layers, which is fractionated in a mild vacuumed distillation column. The column is induced by a steam-jet ejector where steam condensate is produced (sent to biotreatment).
Distillation column bottom also produces wastewater that is sent to the biotreatment facility.
Due to increased customer demand, the plant authority is exploring opportunity to increase the plant overall AN throughput.

## Slide 8: Ex 2.1 – Process description
The stoichiometry equation reveals that water is a by-product for AN production  increased AN production leads to increased wastewater flowrate to the biotretment facility, which is operated at full hydraulic capacity.
Any increase of production capacity is only possible upon the debottlenecking of the biotreatment facility, either by:
  reducing the total wastewater flowrate, or
  installing another biotreatment unit (an expensive strategy).
It is decided to approach the problem by reducing the total wastewater flowrate, by carrying out water recovery between its process sinks and sources.
Task: identify water sinks & sources in order to carry out a water recovery scheme for the process.
Note: ammonia (NH3) concentration is the main concern for water recovery (i.e. the quality index for this case).

## Slide 9: Ex 2.1 – Identification of sources
Reactor
Decanter
Distillation Column
O2
Aqueous layer
Scrubber
NH3
C3H6
Steam-jet Ejector
Steam
Wastewater to Biotreatment
Off-Gas Condensate
Condensate
Bottoms
Water
AN to sales
6.0 kg H2O/s
5.0 kg AN/s
5.1 kg H2O/s
+ Gases
Tail gases to disposal
Boiler
BFW
1.2 kg H2O/s
14 ppm NH3
0.4 kg AN/s
4.6 kg H2O/s
18 ppm NH3
4.6 kg AN/s
6.5 kg H2O/s
10 ppm NH3
4.2 kg AN/s
1.0 kg H2O/s
25 ppm NH3
0.4 kg AN/s
5.5 kg H2O/s
0 ppm NH3
0.1 kg AN/s
0.7 kg H2O/s
1 ppm NH3
3.9 kg AN/s
0.3 kg H2O/s
34 ppm NH3
0.2 kg AN/s
1.2 kg H2O/s
20 ppm NH3
1.1 kg AN/s
12.0 kg H2O/s
Water source ???
Notes: Note to instructor: worksheet print out (black & white setting) will not show the 4 thick arrows of the water source, please get students to mark them on their handout.

## Slide 10: Ex 2.1 – Identification of sources
Following Heuristic 1, the individual streams that contribute to the terminal wastewater stream are segregated as water sources for recovery:
  distillation bottom (0.1 kg/s; 0 ppm)
  off gas condensate (5.0 kg/s; 14 ppm)
  aqueous layer from the decanter (5.9 kg/s; 25 ppm)
  steam condensate from steam-jet ejector (1.4 kg/s; 34 ppm)

## Slide 11: Extraction of limiting data for material sink for concentration-based RCN

## Slide 12: Heuristics 2 & 3
Minimise flowrate for a sink to reduce the overall fresh resource intake.
Maximise the inlet concentration for a sink to maximise material recovery.

## Slide 13: Ex 2.2 – AN production
Reactor
Decanter
Distillation Column
O2
Aqueous layer
Scrubber
NH3
C3H6
Steam-jet Ejector
Steam
Wastewater to Biotreatment
Off-Gas Condensate
Condensate
Bottoms
Water
AN to sales
6.0 kg H2O/s
5.0 kg AN/s
5.1 kg H2O/s
+ Gases
Tail gases to disposal
Boiler
BFW
1.2 kg H2O/s
14 ppm NH3
0.4 kg AN/s
4.6 kg H2O/s
18 ppm NH3
4.6 kg AN/s
6.5 kg H2O/s
10 ppm NH3
4.2 kg AN/s
1.0 kg H2O/s
25 ppm NH3
0.4 kg AN/s
5.5 kg H2O/s
0 ppm NH3
0.1 kg AN/s
0.7 kg H2O/s
1 ppm NH3
3.9 kg AN/s
0.3 kg H2O/s
34 ppm NH3
0.2 kg AN/s
1.2 kg H2O/s
20 ppm NH3
1.1 kg AN/s
12.0 kg H2O/s

## Slide 14: Ex 2.2 – technical constraints
Scrubber
  5.8 ≤ flowrate of wash feed (kg/s) ≤ 6.2
  0.0 ≤ NH3 content of wash feed (ppm) ≤ 10.0
Boiler feed water
  NH3 content = 0.0 ppm
  AN content = 0.0 ppm
Decanter
  10.6 ≤ feed flowrate (kg/s) ≤ 11.1
Distillation column
  5.2 ≤ feed flowrate (kg/s) ≤ 5.7
  0.0 ≤ NH3 content of feed (ppm) ≤ 30.0
  80.0 ≤ AN content of feed (wt%) ≤ 100.0
Upper bound
Lower bound
Upper bound
Lower bound

## Slide 15: Ex 2.2 – Limiting water data
Water sinks, SKj |  | Flowrate | Concentration
j | Stream | FSKj (kg/s) | CSKj (ppm)
1 | Boiler feed water (BFW) | 1.2 | 0
2 | Scrubber | 5.8 | 10
Water sources, SRi |  | Flowrate | Concentration
i | Stream | FSRi (kg/s) | CSRi (ppm)
1 | Distillation bottoms | 0.8 | 0
2 | Off-gas condensate | 5.0 | 14
3 | Aqueous layer | 5.9 | 25
4 | Ejector condensate | 1.4 | 34

## Slide 16: Data extraction for hydrogen-consuming units in refinery

## Slide 17: Refinery hydrogen recovery
Typical hydrogen-consuming units are hydrotreating and hydrocracking processes.
Purge
Recycle
Fresh H2 makeup
Amine unit
High pressure flash separator
Liquid hydrocarbon feed
Reactor
H2S
Liquid product

## Slide 18: Identification of H2 sinks & sources
Purge (FP, CP)
Recycle (FR, CR)
Fresh H2 makeup (FM, CM)
Amine unit
High pressure flash separator
Liquid hydrocarbon feed
Reactor
H2S
Liquid product
Hydrogen sink (FSK, CSK)
Hydrogen source
(FSR, CSR)

## Slide 19: Identification of H2 sinks & sources
Hydrogen sink:
  Flowrate: FSK = FM + FR
  impurity concentration:
  where FSK, FM and FR are the respective flowrates of the hydrogen sink, make-up and recycle streams; with their respective impurity concentrations of CSK, CM and CR.
Hydrogen source:
  Flowrate: FSK = FR + FP
  Concentration: CSK = FR = FP

## Slide 20: Ex 2.4 – Refinery H2 network
Fresh H2 source
Unit A
Unit B
Fuel
Recycle
310 (91%)
Recycle
490 (85%)
Purge
40 (91%)
Purge
10 (85%)
90 (99%)
110 (99%)
200 (99%)

## Slide 21: Ex 2.4 – Refinery H2 network
 | Make-up stream | Recycle stream | Purge stream | Hydrogen sink | Hydrogen source
Unit A |  |  |  |  | 
Flowrate (MMscfd) | 90 | 310 | 40 | 400 | 350
Concentration (%) | 1 | 9 | 9 | 7.20 | 9
Unit B |  |  |  |  | 
Flowrate (MMscfd) | 110 | 490 | 10 | 600 | 500
Concentration (%) | 1 | 15 | 15 | 12.43 | 15

## Slide 22: Data extraction for property integration

## Slide 23: Property integration
Density of the mixture (ρM) is given by:
or the generic form
A generic form of the linearised mixing rule is given as:
ψM(PM) = i xiψi(Pi)
Mixing operation
Mixture
(FM, VM, M)
Solution A
(FA, VA, A)
Solution B
(FB, VB, B)

## Slide 24: Property integration
Example: Mixing of liquid of different density
  1 kg liquid A of 1000 kg/m3 (ρA)
  1 kg liquid B of 1500 kg/m3 (ρB)
Mixture density (ρM) = 1/1000 + 1/1500 = 2/ρM
 ρM = 1200 kg/m3
If we work on the operator of density:
  Liquid A: ψA = 1/1000 = 0.001
  Liquid B: ψB = 1/1500 = 0.0067
  Density operator of mixture, ψM(PM) = i xiψi(Pi)
  ψM = 0.5(0.001) + 0.5(0.0067) = 0.000833
 ρM = 1200 kg/m3

## Slide 25: Reported linearised mixing rule
Property of mixture | Mixing rule | Operator | Reference
Density, |  |  | Shelley and El-Halwagi (2000)
Reid Vapor Pressure, |  |  | Shelley and El-Halwagi (2000)
Material content, |  |  | Shelley and El-Halwagi (2000); El-Halwagi et al. (2002)
Electric resistivity, |  |  | Kazantzi and El-Halwagi (2004)
Viscosity, |  |  | Qin et al. (2004)
Paper reflectivity, |  |  | El-Halwagi et al. (2002)

## Slide 26: Heuristic 4
Choose the property operator of the sink that is furthest from that of the fresh resource.

## Slide 27: Ex 2.5 – Metal degreasing
(Shelley & El-Halwagi, 2002)
Is this the solvent sink?
Thermal processing, solvent regeneration and makeup
Degreasing unit
Metal finishing
To flare
To flare
Organic additives
Degreased metal
Absorber bottoms (to boiler fuel)
5.0 kg/s
2.0 kg/s
Metal
Regenerated solvent
Offgas
Condensate I
(to waste disposal)
4.0 kg/s, 6 atm
Absorption unit
Condensate II
(to waste disposal)
3.0 kg/s, 2.5 atm
Fresh solvent
2.0 atm
Notes: Answer: No, this is not the sink. The 2 process sinks for solvent are absorption and degreasing units.

## Slide 28: Ex 2.5 – Metal degreasing
The fresh solvent has an RVP value of 2.0 atm.
The following process constraints on flowrate and RVP values are to be complied for the process sinks, i.e.:
  Degreasing unit:
  Flowrate of solvent = 5.0 kg/s
  2.0 ≤ RVP of solvent (atm) ≤ 3.0
  Absorption unit:
  Flowrate of solvent = 2.0 kg/s
  2.0 ≤ RVP of solvent (atm) ≤ 4.0

## Slide 29: Ex 2.5 – Metal degreasing
Operator values for sources:
  Fresh solvent - 2.71 atm1.44
  Condensate I - 13.20 atm1.44
  Condensate II - 3.74 atm1.44
Operator values for sinks:
  2.71 ≤ ψ for degreasing unit (atm1.44) ≤ 4.86
  2.71 ≤ ψ for absorption unit (atm1.44) ≤ 7.36

## Slide 30: Ex 2.5 – Metal degreasing
Sink | FSKj (kg/s) | SKj (atm1.44)
Degreasing unit | 5 | 4.86
Absorption unit | 2 | 7.36
Source | FSRi (kg/s) | SRi (atm1.44)
Condensate I | 4 | 13.20
Condensate II | 3 | 3.74
Fresh solvent | To be determined | 2.71

## Slide 31: In-class exercise(s)
Notes: Note to instructors:
This part is optional. May be used when there are excess lecture time.

## Slide 32: P2.5 – N2 recovery
RESIN PREMIXING
SLURRY PREMIXING
DISPERSION
COATING
DRYING
N2
N2
Base film
Additives
Resins
Dispersants and lubricants
Magnetic pigments
Solvent
Binders
Decomposed organics
Gaseous emission
FD = 8.5 kg/s
0.93% solvent
F1 = 3.0 kg/s
C1 = 1.90%
F2 = 5.5 kg/s
C2 = 0.40%
Dry tape product
MEMBRANE
(El-Halwagi, 1997)
Is this the N2 source?
Notes: Answer: Gas emission stream is not the N2 source. The N2 process sources are reject stream from membrane separation & drying units.

## Slide 33: P2.6 – refinery H2 network
CRU
Fresh H2
SRU
NHT
HCU
CNHT
DHT
Fuel
Fuel
41.6 30.0%
69.3 27.0%
277.2 17.9%
304.9 17.9%
512.8
97.0 25.0%
69.3 25.0%
623.8 7.0%
277.2 5.0%
415.8 20.0%
138.6
762.4 6.6%
Units | FR (mol/s) | CR (mol%)
HCU | 1732.6 | 25.0
NHT | 41.6 | 25.0
CNHT | 415.8 | 30.0
DHT | 277.2 | 27.0
Flowrate and concentration of recycle streams in all units:
Tasks: Identify the limiting data in order to carry out a hydrogen recovery analysis

## Slide 34: P2.6 – solution
j | Sinks, SKj | FSKj (mol/s) | CSKi (mol%) |  | i | Sources, SRi | FSRj (mol/s) | CSRi (mol%)
1 | HCU | 2495.0 | 19. 39 |  | 1 | HCU | 1801.9 | 25.0
2 | NHT | 180.2 | 21.15 |  | 2 | NHT | 138.6 | 25.0
3 | CNHT | 720.7 | 24.86 |  | 3 | CNHT | 457.4 | 30.0
4 | DHT | 554.4 | 22.43 |  | 4 | DHT | 346.5 | 27.0
 |  |  |  |  | 5 | SRU | 623.8 | 7.0
 |  |  |  |  | 6 | CRU | 415.8 | 20.0

## Slide 35: P2.7 – wafer fabrication process
Large amount of ultrapure water (UPW) is consumed in a wafer fabrication plant that consist of wet processing section (Wet), lithography, combined chemical and mechanical processing (CMP), & miscellaneous operations (Etc.).
Water quality in considering water recovery is resistivity (R) that reflects the total ionic content in the aqueous streams, with property mixing rule:
UPW
2000 t/h (18 MΩm)
Wet
(7 – 18) MΩm
Lithography
(8 – 15) MΩm
CMP
(10 – 18) MΩm
Etc
(5 – 12) MΩm
500 t/h
450 t/h
700 t/h
350 t/h
250 t/h (1.0 MΩm)
200 t/h (2.0 MΩm)
350 t/h (3.0 MΩm)
200 t/h (2.0 MΩm)
280 t/h (0.5 MΩm)
300 t/h (0.1 MΩm)

## Slide 36: P2.7 – technical info
Operator values for UPW = 0.0556 MΩ-1.m-1
Operator values for sources:
  Wet I - 1 MΩ-1.m-1
  Wet II - 0.5 MΩ-1.m-1
  Lithography - 0.3333 MΩ-1.m-1
  CMP I - 10 MΩ-1.m-1
  CMP II – 0.5 MΩ-1.m-1
  Etc - 2 MΩ-1.m-1
Operator values for sinks:
  0.0556 ≤ ψ for Wet (MΩ-1.m-1) ≤ 0.1429
  0.0667 ≤ ψ for Lithography (MΩ-1.m-1) ≤ 0.1250
  0.0556 ≤ ψ for CMP (MΩ-1.m-1) ≤ 0.1000
  0.0833 ≤ ψ for Etc (MΩ-1.m-1) ≤ 0.2000
Wet
Rmin = 7 MΩ.m  ψ = 0.1429 MΩ-1.m-1
Rmax = 18 MΩ.m  ψ = 0.0556 MΩ-1.m-1
Notes: This slide may be used as worksheet for students.
Worksheet print out (black & white setting) will not show the selection with dotted line, please get students to mark them on their handout.

## Slide 37: P2.7 – solution
Sink | FSKj (kg/s) | SKj (MΩ-1.m-1)
Wet (SK1) | 500 | 0.1429
Litography (SK2) | 450 | 0.1250
CMP (SK3) | 700 | 0.1000
Etc (SK4) | 350 | 0.2000
Source | FSRi (kg/s) | SRi (MΩ-1.m-1)
Wet I (SR3) | 250 | 1
Wet II (SR4) | 200 | 0.5
Litography (SR5) | 350 | 0.3333
CMP I (SR6) | 300 | 10
CMP II (SR7) | 200 | 0.5
Etc (SR8) | 280 | 2