## Slide 1
Chapter 2
Bars and Trusses
Finite Element Modeling and Simulation
with ANSYS Workbench

## Slide 2
Introduction
Figure 2.1. Truss examples: (a) Montreal Biosphere Museum (b) Betsy Ross Bridge.
Trusses are commonly used in the design of buildings, bridges and towers.
This chapter introduces you to the simplest 1-D structural element, the bar element, and the finite element analysis of truss structures using such element.
(a) (b)

## Slide 3
Introduction
Most structural analysis problems can be treated as linear static problem, based on the following assumptions
  Small deformations (loading pattern is not changed due to the deformed shape)
  Elastic materials (no plasticity or failures)
  Static loads (the load is applied to the structure in a slow or steady fashion)
Linear analysis can provide most of the information about the behavior of a structure, and can be a good approximation for many analyses.

## Slide 4
Review of the 1-D Elasticity Theory
x
P
L
A, E
Figure 2.2. An axially loaded elastic bar.
Strain-displacement relation
Strain-displacement relation
Consider a uniform prismatic bar shown below
Equilibrium equation
The displacement, strain and stress field in a bar needs to be solved under given boundary conditions, which can be done readily for a single bar, but can be tedious for a network of bars or a truss structure made of many bars.

## Slide 5
A truss is an assembly of axial bars …
Truss Modeling & Bar Element Formulation

## Slide 6
Figure 2.3. Modeling of a planar roof truss: (a) Physical structure (b) Discrete model.
Modeling of Trusses
For the truss analysis, it is often assumed that
  The bars are of uniform cross sections and joined by frictionless pins.
  Loads are applied to joints only.
Based on the assumptions, truss members are considered to carry only axial loads and have negligible bending resistance.

## Slide 7
Formulation of the Bar Element
Stiffness Matrix – Direct Method
Figure 2.4. Notation for a bar element.
We have
Element equilibrium equation is:
We conclude that the bar behaves like a spring. The element stiffness matrix is:
and
Degree of Freedom (DOF): Number of components of the displacement vector at a node. For 1-D bar element along the x-axis, we have one DOF at each node.
Therefore

## Slide 8
Stiffness Matrix – Energy Approach
Formulation of the Bar Element
Define two linear shape functions as follows
where
Figure 2.5. The shape functions for a bar element.
We can write
where B is the element strain-displacement matrix
and

## Slide 9
Formulation of the Bar Element
Consider the stored strain energy
Stress can be written as
The potential of the external forces is
The total potential of the system is
Setting by the principle of minimum potential energy, we obtain
where
For the bar element

## Slide 10
Formulation of the Bar Element
Treatment of Distributed Load
Figure 2.6. Conversion of a distributed load on one element.
The work done by the equivalent nodal forces are
Distributed axial load q can be converted to two equivalent nodal forces using the shape functions. Consider the work done by the distributed load q.

## Slide 11
Formulation of the Bar Element
Setting
, we obtain the equivalent nodal force vector
If q is a constant, we have
Figure 2.7. Conversion of a distributed load with constant intensity q on two elements.

## Slide 12
Formulation of the Bar Element
Bar Element In 2-D and 3-D
2-D Case
Figure 2.8. Local and global coordinates for a bar in 2-D space.

## Slide 13
Formulation of the Bar Element
Displacement vectors in the local and global coordinates are related as follows
where
In matrix form
For the two nodes of the bar element, we have
or
In matrix form
with

## Slide 14
Formulation of the Bar Element
In the local coordinate system, we have
or
Augmenting this equation, we write

## Slide 15
Formulation of the Bar Element
Using the transformations, we obtain
Thus, the element stiffness matrix k in the global coordinate system is
The explicit form

## Slide 16
Formulation of the Bar Element
3-D Case
Figure 2.9. Local and global coordinates for a bar in 3-D space.

## Slide 17
Formulation of the Bar Element
The transformation relation is
FEM software packages will do this transformation automatically.
The input data for bar elements are simply the coordinates (X, Y, Z) for each node, E and A for each element (Length L can be computed from the coordinates of the two nodes).
where
x, y and z coordinate axis in the global coordinate system, respectively.
are the direction cosines of the local

## Slide 18
Formulation of the Bar Element
Element Stress
Once the nodal displacement is obtained for an element, the stress within the element can be calculated using the basic relations.
For 2-D cases, we proceed as follows
which is a general formula for 2-D bar elements.
That is,

## Slide 19
We now look at examples of 1-D stress and plane truss problems …
Examples with Bar Elements

## Slide 20
Examples with Bar Elements
x
1
2
3
L
A, E
2A, E
P
1
2
L
Example Problems
Example 2.1
Problem: Find the stresses in the two-bar assembly which is loaded with force P, and constrained at the two ends.
Solution: Use two 1-D bar elements.

## Slide 21
Examples with Bar Elements
For element 1,
For element 2,
Assemble the global FE equation as follows

## Slide 22
Examples with Bar Elements
Load and boundary conditions (BCs) are
FE equation becomes
Thus,

## Slide 23
Examples with Bar Elements
Stress in element 1 is
Similarly, stress in element 2 is
Check the results: Draw the FBD and check the equilibrium of the structures.

## Slide 24
Examples with Bar Elements
x
1
2
3
L
L
A, E
P
1
2

Example 2.2

## Slide 25
Examples with Bar Elements
We first check to see if contact of the bar with the wall on the right will occur or not. To do this, we imagine the wall on the right is removed and calculate the displacement at the right end.
Thus, contact occurs and the wall on the right should be accounted for in the analysis.
The global FE equation is found to be

## Slide 26
Examples with Bar Elements
The load and boundary conditions are
FE equation becomes
Solving this, we obtain

## Slide 27
Examples with Bar Elements
To calculate the support reaction forces, we apply the 1st and 3rd equations in the global FE equation.
Check the results!

## Slide 28
Examples with Bar Elements
Example 2.3
A simple plane truss is made of two identical bars (with E, A, and L), and loaded as shown in the above figure.
Find:
(a) displacement of node 2;
(b) stress in each bar.

## Slide 29
Examples with Bar Elements
In local coordinate systems, we have
Element 1:
Element 2:

## Slide 30
Examples with Bar Elements
Assemble the structure FE equation
Load and boundary conditions (BC)
Condensed FE equation

## Slide 31
Examples with Bar Elements
Solving this, we obtain
Stresses in the two bars

## Slide 32
Examples with Bar Elements
Example 2.4 (Multipoint Constraint)

## Slide 33
Examples with Bar Elements
Element 1:
Element 2:
Element 3:

## Slide 34
Examples with Bar Elements
The global FE equation is
Load and boundary conditions (BCs)

## Slide 35
Examples with Bar Elements
From the transformation relation and the BC, we have
that is
Similarly, we have a relation for the force at node 3
that is
This is a multipoint constraint (MPC).

## Slide 36
Examples with Bar Elements
Applying the load and BC’s in the structure FE equation by “deleting” the 1st, 2nd and 4th rows and columns, we have
Further, from the MPC and the force relation at node 3, the equation becomes
which is

## Slide 37
Examples with Bar Elements
Solving this, we obtain the displacements
From the global FE equation, we can calculate the reaction forces

## Slide 38
Case Study with ANSYS Workbench
Analysis of a truss bridge …

## Slide 39
Case Study with ANSYS Workbench
<Problem Description> Truss bridges can span long distances and support heavy weights without intermediate supports. They are economical to construct and are available in a wide variety of styles. Consider the following planar truss, constructed of wooden timbers, which can be used in parallel to form bridges. Determine the deflections at each joint of the truss under the given loading conditions.
1m
1m
1m
1m
1m
Material: Douglas Fir
E = 13.1 GPa
ν = 0.29
Member cross section:
height = 6 cm
width = 6 cm
30kN
30kN
30kN

## Slide 40
Case Study with ANSYS Workbench
Step 1: Start an ANSYS Workbench Project
Launch ANSYS Workbench and save the blank project as ‘Woodtruss.wbpj’.
Step 2: Create a Static Structural (ANSYS) Analysis System

## Slide 41
Case Study with ANSYS Workbench
Step 3: Add a New Material
Double-click on the Engineering Data cell in the above Project Schematic to edit or add a material. In the following Engineering Data interface which replaces the Project Schematic, click the empty box highlighted below and type a name, ‘Douglas Fir’, for the new material.

## Slide 42
Case Study with ANSYS Workbench
Select ‘Douglas Fir’ from the Outline window, and double-click Isotropic Elasticity under Linear Elastic in the leftmost Toolbox window. Enter ‘1.31E10’ for Young’s Modulus and ‘0.29’ for Poisson’s Ratio in the bottom center Properties window.

## Slide 43
Case Study with ANSYS Workbench
Step 4: Launch the DesignModeler Program
Ensure Line Bodies is checked in the Properties of Schematic A3: Geometry window. Double-click the Geometry cell to launch DesignModeler, and select ‘Meter’ as length unit in the Units pop-up window.

## Slide 44
Case Study with ANSYS Workbench
Step 5: Create Line Sketch
Click the Sketching tab and select Settings. Turn on Show in 2D and Snap under Grid options.
Draw 13 lines as shown in the sketch below. After completion, click Generate to create a line sketch.

## Slide 45
Case Study with ANSYS Workbench
Step 6: Create Line Body from Sketch
Check off the Grid options under Settings of Sketching Toolboxes. Switch to the Modeling tab. Note that a new item named Sketch1 now appears underneath XYPlane in the Tree Outline.
Select Sketch1 from the Tree Outline and click Apply to confirm on the Base Objects selection in the Details of Line1. Click Generate to complete the line body creation.

## Slide 46
Case Study with ANSYS Workbench
Step 7: Create a Cross Section
Select a Cross Section of Rectangular from the Concept drop-down menu. A new item named Rect1 is now added underneath the Cross Section in the Tree Outline. In the Details of Rect1 under Dimensions, enter ‘0.06m’ for both B and H.

## Slide 47
Case Study with ANSYS Workbench
Step 8: Assign Cross Section to Line Body
Select the Line Body underneath 1Part, 1 Body in the Tree Outline. In the Details of Line Body, assign Rect1 to the Cross Section selection. Click Close DesignModeler to exit the program.

## Slide 48
Case Study with ANSYS Workbench
Step 9: Launch the Static Structural (ANSYS) Program
Double-click the Model cell to launch the Static Structural (ANSYS) program. Note that in the Details of “Line Body” the material is assigned to Structural Steel by default. Click to the right of the Assignment field and select Douglas Fir from the drop-down context menu.

## Slide 49
Case Study with ANSYS Workbench
Step 10: Generate Mesh
In the Details of “Mesh”, enter a fairly large number, say,‘10m’, for the Element Size, to ensure each member is meshed with only one element. In the Outline of Project, right-click on Mesh and select Generate Mesh.

## Slide 50
Case Study with ANSYS Workbench
Step 11: Apply Boundary Conditions
In the Outline of Project, right-click on Static Structural (A5) and select Insert and then Fixed Support. After completion, a Fixed Support item is added underneath Static Structural (A5) in the project outline tree.

## Slide 51
Case Study with ANSYS Workbench
Step 12: Apply Loads
In the Outline of Project, right-click on Static Structural (A5) and select Insert and then Force. In the Details of “Force”, click Apply to confirm on the Geometry selection. Also underneath the Details, change the Define By selection to Components and enter ‘-90000N’ for the Y Component.

## Slide 52
Case Study with ANSYS Workbench
Step 13: Retrieve Solution
Insert a Total Deformation item by right-clicking on Solution (A6) in the Outline tree.
Right-click on Solution (A6) in the Outline tree and select Solve. The program will start to solve the model. After completion, click Total Deformation in the Outline to review the total deformation results.

## Slide 53
Summary
In this chapter,
We study the bar elements which can be used in truss analysis.
The concept of the shape functions is introduced and the derivations of the stiffness matrices using the energy approach are introduced.
Treatment of distributed loads is discussed and several examples are studied.
A planar truss structure is analyzed using ANSYS Workbench. It provides basic modeling techniques and shows step-by-step how Workbench can be used to determine the deformation and reaction forces in trusses.