## Slide 1: MECHANICS OF MATERIALS: WITH APPLICATIONS IN EXCEL CHAPTER 2: TORSIONAL LOADS
LECTURE 7
2.1 INTRODUCTION
2.2 INTERNAL TORQUE

## Slide 2: Lecture Outline
Introduction
Internal Torque
Examples

## Slide 3: Introduction
This topic deals with members subjected to torsional loads, namely, moments (couples) about the centroidal axes of such members.
These types of moments or couples are generally referred to as torques and the members subjected to torques are generally known as shafts.
Examples of these types of members include propeller shafts of ships and aircraft and drive shafts of automobiles, power tools, and other equipment.

## Slide 4: Concentrated Torque
A concentrated torque may be defined as one that is applied over a very small area (assumed to be a point) of the member on which it acts.

## Slide 5: Distributed Torque
A distributed torque is applied over the length of a member.

## Slide 6: Internal Torque
Internal torque at any location along the member is obtained by introducing a section at the location and applying equilibrium. The figure below illustrates the internal torque at C, TC.

## Slide 7: Sign Convention
Torque is positive, if the two-headed vector representing it points away from the surface on which it acts, and negative, if it points into this surface.

## Slide 8: Internal Torque Diagram
An internal torque diagram is a diagram that shows, at a glance, how the internal torque changes from point to point along the length of the shaft

## Slide 9: Examples