## Slide 1: Sample vs Population
(true mean)
(true variance)
(sample mean)
(sample variance)

## Slide 2: Populations Parameters and Sample Statistics
A sample is a finite-member representation of an
‘infinite’-member population.
Sample statistics include its sample mean, variance
and standard deviation (square root of the variance):

## Slide 3: Populations Parameters and Sample Statistics
Population parameters include its true mean, variance
and standard deviation (square root of the variance):
Sample statistics with statistical inference can be used
to estimate their corresponding population parameters
to within an uncertainty.

## Slide 4: Comparing Theory and Measurement
Agreement between theory and experiment does NOT
imply correctness.
Counter-examples include:
  bad theory agreeing with bad data
  bad theory agreeing with good data by coincidence
  good theory agreeing with bad data because a variable
  was not considered or controlled in the experiment
Scientific information can be misused selectively.
Comparisons must be made within the context of
uncertainty.

## Slide 5: Figure 9.1
Proper Graphical Comparison with Uncertainty

## Slide 6: How Sure Are We ?
When a physical process is quantified, uncertainties associated with describing the process occur.
Uncertainties result from
Experiments Modeling
Instruments:
calibration and use
Experimental Process
Data Manipulation:
fitting and analysis
Analytical Model Assumptions
Numerical Model Approximations

## Slide 7: Systematic and Random Uncertainties
Uncertainties are categorized as either systematic (bias)
or random (precision).
An uncertainty is assumed to be systematic if no
statistical information is provided.
An uncertainty is an estimate of the error.
An error is the difference between the measured and
the true value.

## Slide 8: Systematic and Random Uncertainties
Systematic, Bi:
arises from comparisons with standards (calibration)
involves no statistics; the number is given alone
related to the accuracy (‘to within Bi units’)
Random, Pi:
based upon repeated measurements
involves statistics ( )
related to the precision (scatter)
for one more measurement
for multiple measurements

## Slide 9: Figure 9.2
Systematic and Random Uncertainties
based upon comparison between
sample and true (population) means
based upon N and Sx

## Slide 10: Precision and Accuracy
Precision Accuracy
good poor
good good
poor poor