## Slide 1: Amplifiers and Filters
amplifiers, filters

## Slide 2: Amplifiers
An amplifier is an electronic component that scales
the magnitude of a signal from its input value, Ei,
to its output value, Eo.
Functionally, this can be expressed as Eo = f[Ei],
where f is some amplification operator.
For a linear amplifier, Eo = G•Ei, where G is the gain.
For a logarithmic amplifier, Eo = G•log[Ei].

## Slide 3: Figure 6.4: The LM124 Series Op Amp
Operational Amplifiers

## Slide 4: Operational Amplifiers
Figure 6.5
The complex circuit of the op amp can be modeled
as a ‘black box’ having two voltage inputs and one
voltage output.
It major attributes are:
[1] very high input impedance (> 107 Ω)
[2] very low output impedance (< 100 Ω)
[3] high internal open-loop gain (~105 to 106)

## Slide 5
Differential Op Amp Equation
Kirchoff’s First Law can be applied to determine the amplification
factor for this configuration.
at node A, (Ei2-EA)/R1 = (EA-0)/R2
A
B
at node B, (Ei1-EB)/R1 = (EB-Eo)/R2
Now EA = EB because the voltage difference between the inputs is
zero (a consequence of the op amp’s high internal open-loop gain).
Equating the two expressions yields the desired factor.

## Slide 6: Figure 6.7

## Slide 7: Filters
A filter removes a signal’s unwanted frequency components.
A filter alters both the magnitude and the phase of the signal.
The time constant of a simple RC filter equals RC. A unit balance gives:
   (s) = R (V/A) • C (C/V) = (C/A) = (C / [C/s]) = (s)

## Slide 8
Figure 6.9
Filter Terminology
cut-off frequencies
for simple filters, c = 1/RC
or fc = 1/(2RC)

## Slide 9: Simple RC Filters
Low Pass Filter:
Passes low-frequencies
Removes high-frequencies
High Pass Filter:
Passes high-frequencies
Removes low-frequencies
Figure 6.10

## Slide 10: Filter Distortion of Signal
Figure 6.11
A filter alters the signal by
introducing
a phase lag
and a magnitude attenuation
low-pass
high-pass
circular frequency for this signal =
cyclic frequency for this signal =
 = 2f = ~ 1 rad/s
f = ~1 cycle / 6.4 s = ~0.16 Hz