## Slide 1: Calibration and Static Response
Measurement systems and their individual components ‘respond’ to inputs by producing an output for a given input.
The output can differ from the input by having a different frequency and amplitude, and also a phase lag (time delay).
For linear systems, the frequency is not altered. However, the output can have an amplitude that is different than the input, and the output can lag the input.
System response can be subdivided into static and dynamic responses.
Static implies invariant in time; dynamic variant in time.

## Slide 2: A Static Calibration
Figure 5.1
The slope of the static calibration curve is the sensitivity, K.
K=K(x) → many different values of K for a given curve.
Usually a high static sensitivity is desired (this leads to a lower x-from-y uncertainty.

## Slide 3: Calibration Terms
Calibration is the comparison of a measured value to a known,
much more accurate value, known as the true value.
The absolute error is the difference between the measured and true values.
The relative error is the ratio of the absolute error over the true value.
The accuracy of the calibration equals 1 - relative error.
When a calibration consists of a number of comparisons, the maximum
relative error often is used to characterize the calibration.

## Slide 4: In-Class Example