## Slide 1: Response Characterization
The output, y(t), of a linear system can be determined by
by solving the linear ODE
in which the a’s are constant coefficients, n the order of the
system, and F(t) the forcing function.
y(t) can represent a physical variable that varies in time,
such as pressure, temperature, velocity, …
The exact ODE that describes the system is derived from
a conservation law.

## Slide 2: Example First-Order System
Consider the response of a bulb thermometer
that is immersed from room air into hot water.
Heat is transferred from the hotter water through
glass wall into the cooler liquid inside the bulb.
E = total energy (J); Q = heat transfer (J); t = time (s)
This thermal energy transfer is governed by the first law of thermodynamics.
Heat is transferred convectively to the glass from the hot water as
h = heat transfer coefficient (W / [m2K]);
A = surface area of heat transfer
This is known as Fourier’s law.

## Slide 3
Assume that all of the heat transferred from the hot water through the glass
reaches the liquid inside the bulb, thereby increasing the temperature of the
liquid. Conservation of energy requires that
m = mass of the liquid (kg); Cv = specific heat at
constant volume of the liquid (J / [kg K])
Combining the previous equations gives
This is a linear, first-order ordinary differential equation, which is of the form
Here, y = T, K = 1, Thw = F(t), and = mCv/hA.

## Slide 4: Lower-Order Systems
For a zero-order system (n=0),
Examples: strain gage, pitot-static tube
For a first-order system (n=1),
Examples: thermometer, RC circuit
For a second-order system (n=2),
Examples: pressure transducer, accelerometer,
RLC circuit