## Slide 1: Examining the Signal
Examine the signal using a very high-speed system, for example, a 50 MHz digital oscilloscope.
  What is the order of the signal’s frequency range (fmin to f max)?
How is the signal characterized?

## Slide 2: Setting the Sampling Conditions
In most circumstances, as when using computers, sampling is DIGITAL.
How many samples (data points) should be taken ?
What resolution in time and/or frequency is required ?

## Slide 3: The Number of Samples
The number of required samples depends upon what information is needed
→ there is not one specific formula for N..
For example, consider two different signals
Solid: ‘normal’ (random) population with mean =3 and standard deviation = 0.5
Dotted: same as solid but with 0.001/s additional amplitude decrease

## Slide 4: Digital Sampling
Figure 12.1
The analog signal, y(t), is sampled every t seconds, N times for a period
of T seconds, yielding the digital signal y(rt), where r = 1, 2, …, N.
For this situation:

## Slide 5: Digital Sampling Errors
When is signal is digitally sampled, erroneous results occur if either one
of the following occur:
the sample period is incorrect
the sampling rate is too low
To avoid aliasing, set fs > 2 fmax.
Aliased frequencies can be determined using the folding diagram.
The maximum frequency of interest, fmax, also is called the Nyquist frequency, fN.
So, to avoid aliasing, set fs > 2 fN.

## Slide 6: Digital Sampling Errors
The least common multiple or lowest common multiple or smallest common multiple of two integers a and b is the smallest positive integer that is a multiple of both a and b. Since it is a multiple, a and b divide it without remainder. For example, the least common multiple of the numbers 4 and 6 is 12. (Ref: Wikipedia)
To avoid amplitude ambiguity, set the sample period equal to the least
common (integer) multiple of all of the signal’s contributory periods.
For a signal with only one period, T1, set T = mT1 = m/f1.
Recall T = Nt = N/fs. → fs = (N/m) f1.

## Slide 7: Digital Sampling Errors
If all of the frequencies are known (deterministic, simple or complex periodic signals), the sample period can be determined exactly and amplitude ambiguity can be eliminated.
If some of the frequencies are not known (nondeterministic signal), amplitude ambiguity can not be eliminated but can be minimized by ‘windowing’ the signal.

## Slide 8: Illustration of Correct Sampling
y(t) = 5sin(2t)
→ f = 1 Hz
with fs = 8 Hz
Figure 12.7

## Slide 9
y(t) = sin(20t)
→ f = 10 Hz
with
fs = 12 Hz
Aliasing of sin(20t)