## Slide 1
y(t) = sin(20t)
→ f = 10 Hz
with
fs = 12 Hz
digital signal
appears to
have frequency
of 2 Hz
Aliasing of sin(20t)

## Slide 2: Figures 12.8 and 12.9
The Folding Diagram
Example: f = 10 Hz; fs = 12 Hz
3. Calculate the aliased frequency,,where
fa = kafN =kafs/2
To determine the
aliased frequency, fa:
1. Determine k, where
k = f/fN = 2f/fs
2. Using the folding diagram, find the ka, into which k folds.
→ k = 20/12 = 1.67
→ ka = 0.33
→ fa = (0.33)(12/2) = 2 Hz

## Slide 3: Aliasing of sin(20t)
Aliasing occurs
because of
low sample rate
y(t) = 5sin(2t)
→ f = 1 Hz
fs = 1.33 Hz
Figure 12.13

## Slide 4: In-Class Example
At what cyclic frequency will y(t) = 3sin(4t) appear if fs = 6 Hz?
2 Hz (f/fN = 2f/fs = 4/fs < 1 → no aliasing)
fs = 4 Hz ?
fs = 2 Hz ?
2 Hz (f/fN = 2f/fs = 4/fs = 1)
0 Hz (f/fN = 2f/fs = 4/fs = 2 → aliasing to 0fN)
fs = 1.5 Hz ?
0.5 Hz (f/fN = 2f/fs = 4/fs = 8/3
→ aliasing to 2fN/3 = fs/3 = 0.5)

## Slide 5: Correct Sample Time Period
y(t) =
3.61sin(4t+0.59)
+ 5sin(8t)
f’s of 2 Hz and 4 Hz
→
T’s = 0.5 s and 0.25 s
→
use T = m(0.5) s
m = 1 or 2 or 3 …
Figure 12.16

## Slide 6: Sampling with Aliasing
Sample ended
at cycle’s end
→ correct
amplitude
BUT aliasing
occurs because
of low sample rate
y(t) = 5sin(2t)
→ f = 1 Hz
fs = 1.33 Hz
Figure 12.13

## Slide 7: Sampling with Amplitude Ambiguity
Sample NOT
ended at
cycle’s end
→ false
amplitudes
y(t) = 5sin(2t)
→ f = 1 Hz
fs = 3.33 Hz
Figure 12.12

## Slide 8: y(t) = 6 + 2sin(t/2) + 3cos(t/5) +4sin(t/5 + ) – 7sin(t/12)
Smallest sample period that contains all integer multiples of the Ti’s:
120 s
1/4 1/10 1/10 1/24
fi (Hz):
Ti (s):
4 10 10 24
→ T can be set at 120, 240, 360, … to avoid amplitude ambiguity
Smallest sampling to avoid aliasing (Hz):
fs > 2 fmax = 0.5 Hz
In-Class Example