## Slide 1: Measurement Systems

## Slide 2: Measurement Hardware
Sensor: a device that senses a physical
stimulus and converts it into a signal.
Transducer: a device that changes the
signal into the desired form.
Signal Conditioner: a device that puts the
signal into its final form to be processed
and recorded.
Signal Processor: a device that converts
the signal typically from analog to digital
and stores the information.

## Slide 3: A Simple Measurement System
Sensor:
Transducer:
Signal Conditioner:
Signal Processor:
liquid
bulb
stem
scale on stem
liquid
bulb
stem
scale

## Slide 4: Some Sensors
Is this a sensor?
NO !
strain gage
(R=L/A)
hot-film probe
(or RTD)
R=Ro[1+(T-To)]
thermistor
R=Roexp[(1/T-1/To)]

## Slide 5: In-Class Example
Figure 4.18
RTD: RTD = 0.0005 / ºC; R = 25  at 20.0 ºC
Bridge: R2 = R3 = R4 = 25 Ei =5 V
Amplifier: Gain = G
Multimeter: +10 V maximum

## Slide 6: In-Class Example
Find [a] R() at 67 ºC; [b] Eo(V) at 78 ºC; [c] G to give +10V
at max. temperature condition of 78 ºC; [d] Em (V) at 60 ºC.
[a] R = Ro[1+(T-To)]
>> R67 ºC = R20 ºC[1+0.0005(67-20)]
= (25)(1.0235) = 25.588 
[b] R78 ºC = R20 ºC[1+0.0005(78-20)] = (25)(1.029) = 25.725 
R =R78 ºC – R20 ºC = 25.725 – 25 = 0.725 
All R’s initially the same >> Eo = Ei[(R/R)/(4+2R/R)]
Thus, Eo = 0.145/4.058 = 0.0357 V.

## Slide 7: In-Class Example
[c] G = amp.output / amp. input
= Em/Eo = 10/0.0357 = 210.11 >> set at 200.
[d] R60 ºC = R20 ºC[1+0.0005(60-20)] = (25)(1.02) = 25.5 
R =R60 ºC – R20 ºC = 25.5 – 25 = 0.5 
Eo = Ei[(R/R)/(4+2R/R)] = 0.1/4.04 = 0.0248 V
Em = G Eo = (200)(0.0248) = 4.95 V