## Slide 1: Measurement Uncertainty Analysis
Overall goal:
Obtain an estimate of Ux, where
  x' = x ± Ux (%C)
  x can be either a single value or an average value.
The magnitude of Ux depends upon %C, the contributing
uncertainties, and how these contributing uncertainties
are combined.

## Slide 2: Measurement Uncertainty Analysis
The overall uncertainty, Ux, is related to the combined
standard uncertainty, uc, through a coverage factor, where
For most experiments, ≥ 10 >> t,95 ≈ 2 (<10 % error).
This implies Ux,95 ≈ 2uc = . This is called the large
scale approximation.

## Slide 3: Table 8.4
Student’s t Table
Gives the value of t for a given  and P % confidence .
Examine P = 95 %
What is t for N = 12 ?
N = 12
>>  = N – 1 = 11
t11,95 = 2.201

## Slide 4: Quadrature Combination of Uncertainties
The combined standard uncertainty, uc, comes from the
combined estimated variance, uc2, which is expressed as:
assuming each xi is independent of the other J-1 variables.
i is the absolute sensitivity coefficient, which weights the
uncertainty contribution of xi to the result.
i = 1 for a measurand.
r denotes a result (a variable that is a function of one or
more measurands)

## Slide 5: In-Class Example
Determine the combined standard uncertainty in the dynamic pressure, up, where p = ½  V2. The measurement uncertainties are u = 0.03 kg/m3 and uV = 0.02 m/s. Assume nominal values of  = 1.16 kg/m3 and V = 1 m/s.
So, up = 0.028 Pa

## Slide 6: In-Class Example (cont’d)
What is the overall uncertainty in the dynamic pressure assuming the results were based upon a large number of measurements and 95 % confidence?
The large scale approximation gives
Up ≈ 2up = (2)(0.028) = 0.056 Pa

## Slide 7: Tracking Down Uncertainties
Uncertainties for an experiment can arise from
instruments (resolution, instrument uncertainties)
experimental conditions (temporal variations, …)
data manipulation (curve fitting, finite differencing, …)
We will focus on characterizing the first two sources
of uncertainties. Some of the third (primarily related
to curve fitting) will be considered later.

## Slide 8: Temporal Precision Uncertainty
When an experiment is conducted under ‘fixed’ operating conditions, the measurand signal still may vary somewhat in time. This results from uncontrolled ‘extraneous’ variables that change in time.
This ‘temporal precision’ uncertainty can be estimated as:
ut(x) = t,PSx/√N