## Slide 1: 1700’s T, p, RH Measurement System
pressure
temperature
relative
humidity

## Slide 2: First-Order System Dynamic Response
The general expression for a first-order system is
This is a linear first-order ODE, which can be rearranged as
The time constant of the system, , equals a1/a0. K (=1/a0) is a constant that converts F(t) into units of y.
The general expression is a physical law for the system, such as conservation of energy (Kirchhoff’s voltage law) for a simple RC circuit.
= RC for a RC circuit and  = mCv/hA for a thermocouple.

## Slide 3: Dynamic Response to F(t)
The exact solution of depends upon the
specific type of forcing function, F(t).
We will study the responses to two different forcing functions.
Step: F(t) = 0 for t ≤ 0 and F(t) = A for t > 0
Sinusoidal: F(t) = A sin(t)
amplitude
circular frequency
(rad/s)
F(t) = 0
F(t) = A
t = 0
t →
+A
-A
0
t →

## Slide 4: Step-Input Forcing
The general solution for step-input forcing is of the form
Substitution of this equation into the governing equation gives
The initial condition, y(t = 0) = y0 = c0 + c1, gives
Thus, the specific solution is

## Slide 5: Step-Input Forcing
Also, y∞ = y(t = ∞) = KA.
Using the above expressions and defining the magnitude ratio, M, results in
The dynamic error, (t), relates to the magnitude ratio as

## Slide 6
Figure 5.2
Step-Input Forcing
0.632
0.99

## Slide 7: In-Class Example
For a RC circuit (R = 2 ; C = 0.5 F) with step input forcing from 0 V to 1 V:
  What is the V of the circuit at 1 s ?
  What is the V of the circuit at 5 s ?
0.6321 V (0.6321V at t =  )
  What is the % dynamic error at 1 s ?
36.79 ( = 1 - M)
~1.0 V (>0.99V at t = 5 )

## Slide 8: Sinusoidal-Input Forcing
The general solution for sinusoidal-input forcing is of the form
Substitution into the governing equation, comparing like terms (see Exmpl. 5.4), and using the initial condition y(0) = y0 with input forcing F(t)=Asin(ωt) gives
transient response
steady-state response
The phase lag, (in radians), shifts the output in time from the input, where  = -tan-1().

## Slide 9
Figure 5.5
Sinusoidal-Input Forcing
 is the
phase lag in
units of seconds
output lags input
in time
output amplitude
< input amplitude

## Slide 10: Sinusoidal-Input Forcing
Figures 5.3 and 5.4

## Slide 11: In-Class Example
For a RC circuit (R = 2 ; C = 0.5 F) with sine input
forcing of 3sin(2t) from 0 V to 1 V:
  What is its phase lag in degrees?
  What is its phase lag in s ?
  What is its magnitude ratio ?
-(180/)tan-1() = -63.43
-0.55 s [ = -tan-1(
0.448 [M = 1/√(1+ 
NOTE: The minus sign in the phase lag simply means
that the output lags the input in time.

## Slide 12: Sinusoidal-Input Forcing
 = 2
 = 2
 = -63.43
M = 0.448
10
20
50
0.2