## Slide 1: Calibration and Static Response
Measurement systems and their individual components ‘respond’ to inputs by producing an output for a given input.
The output can differ from the input by having a different frequency and amplitude, and also a phase lag (time delay).
For linear systems, the frequency is not altered. However, the output can have an amplitude that is different than the input, and the output can lag the input.
System response can be subdivided into static and dynamic responses.
Static implies invariant in time; dynamic variant in time.

## Slide 2: A Static Calibration
Figure 5.1
The slope of the static calibration curve is the sensitivity, K.
K=K(x) → many different values of K for a given curve.
Usually a high static sensitivity is desired (this leads to a lower x-from-y uncertainty.

## Slide 3: Calibration Terms
Calibration is the comparison of a measured value to a known,
much more accurate value, known as the true value.
The absolute error is the difference between the measured and true values.
The relative error is the ratio of the absolute error over the true value.
The accuracy of the calibration equals 1 - relative error.
When a calibration consists of a number of comparisons, the maximum
relative error often is used to characterize the calibration.

## Slide 4: In-Class Example

## Slide 6: Response Characterization
The output, y(t), of a linear system can be determined by
by solving the linear ODE
in which the a’s are constant coefficients, n the order of the
system, and F(t) the forcing function.
y(t) can represent a physical variable that varies in time,
such as pressure, temperature, velocity, …
The exact ODE that describes the system is derived from
a conservation law.

## Slide 7: Example First-Order System
Consider the response of a bulb thermometer
that is immersed from room air into hot water.
Heat is transferred from the hotter water through
glass wall into the cooler liquid inside the bulb.
E = total energy (J); Q = heat transfer (J); t = time (s)
This thermal energy transfer is governed by the first law of thermodynamics.
Heat is transferred convectively to the glass from the hot water as
h = heat transfer coefficient (W / [m2K]);
A = surface area of heat transfer
This is known as Fourier’s law.

## Slide 8
Assume that all of the heat transferred from the hot water through the glass
reaches the liquid inside the bulb, thereby increasing the temperature of the
liquid. Conservation of energy requires that
m = mass of the liquid (kg); Cv = specific heat at
constant volume of the liquid (J / [kg K])
Combining the previous equations gives
This is a linear, first-order ordinary differential equation, which is of the form
Here, y = T, K = 1, Thw = F(t), and = mCv/hA.

## Slide 9: Lower-Order Systems
For a zero-order system (n=0),
Examples: strain gage, pitot-static tube
For a first-order system (n=1),
Examples: thermometer, RC circuit
For a second-order system (n=2),
Examples: pressure transducer, accelerometer,
RLC circuit