## Slide 1
A Sign in Penacook, New Hampshire
Basic Electronics

## Slide 2: I, V Relations for R, L and C (Table 4.1)
Element | Unit Symbol | I(t) | V(t) | VI=const
Resistor | R | V(t)/R | RI(t) | RI
Capacitor | C | CdV(t)/dt | (1/C)∫I()d | It/C
Inductor | L | (1/L)∫V()d | LdI(t)/dt | 0

## Slide 3: R, L and C Combinations
Figures 4.5 and 4.6
Series:
R, L and 1/C add
Parallel:
1/R, 1/L and C add

## Slide 4: Basic Electronics – R, C and L
For R, C, and L combination in series:
Potential Difference:
Current:
V(t) = IR + (1/C)∫I()d + LdI/dt
For R, C, and L combination in parallel:
Potential Difference:
Current:
I(t) = V/R + CdV/dt + (1/L)∫V()d
I(t) = V/R = CdV/dt = (1/L)∫V()d
V(t) = IR = (1/C)∫I()d = LdI/dt

## Slide 5: Basic Electronics – R, C and L
Current related to charge
Determine the DC potential difference across
2 inductors in parallel:
V(t) = LTdI/dt = [L1L2/(L1+L2)]dI/dt = 0
I(t) = dq/dt
A=C/s
DC: direct current →
DC: alternating current →
dI/dt = 0
dI/dt ≠ 0

## Slide 7: Kirchhoff’s Laws
Node: a point in a circuit where any two of more elements meet
Loop: a closed path going from one circuit node back to itself
without passing through any intermediate node more
than once
Kirchhoff’s first (or current) law: at a circuit node, the current
flowing into the node equals the current flowing out
(charge is conserved)
Kirchhoff’s second (or voltage) law: around a circuit loop,
the sum of the voltages equal zero
(energy is conserved)

## Slide 8: Example RLC Circuit
Consider a RLC circuit used in your ‘Dynamic System
Response’ laboratory exercise.
Using Kirchoff’s Voltage Law, determine the governing
expression for this circuit.

## Slide 9
R
Ei, R, L and C are in series →
Recall that I=dQ/dt →
This is a linear,
2nd-order ODE.

## Slide 10
Now examine another loop and apply Kirchoff’s Voltage
Law again.
So, to find Eo, we must first find Q → we must integrate
the previous 2nd-order ODE.
The solution is presented in Appendix H of the text.

## Slide 11: The Wheatstone Bridge
Figure 4.10
Use Kirchhoff’s Voltage Law:
Ei = I1R1 + I2R2
Ei = I3R3 + I4R4
Eo = I4R4 - I2R2
Eo = -I3R3 + I1R1
Further, I1 = I2 and I3 = I4.
Combining these equations gives

## Slide 12
What is the Wheatstone
bridge equation if another
resistor, Rx, is added in
parallel with R1 ?
Rx
Now 1/Rnew = 1/Rx+1/R1
To solve, simply substitute
Rnew = R1Rx / (R1+Rx)
into the WB equation for R1.

## Slide 13
One advantage of using two resistors in parallel in
one leg of the WB is that the added resistor can be
located remotely from the actual WB, such as in a flow.
Here, that resistor can serve as a sensor.
Rx
FLOW