## Slide 1: Chapter 1 - Experiments
An experiment is performed to determine the velocity profile along a wind tunnel’s test section using a pitot-static tube. Identify the independent, dependent, extraneous and parameter variables.
Tunnel rpm
Station position
Environment p and T

p
U
parameter
independent
independent, extraneous ?
dependent
dependent
dependent

## Slide 2: Chapter 2 - Units
Your brain weighs 8.0 pounds on Earth. Find
SI weight =
SI mass on Pluto (gPluto = 0.05 gEarth)
Age of our universe
= 13.7 Gy
~ 32 N
mPluto = mEarth = W/g = 32/9.8 = ~ 3.3 kg
Weight in pounds on Pluto
(mg)Pluto = ~(3.3)(0.05)(9.81)/4 = ~ 0.40 lbf

## Slide 3: Chapter 2 – Significant Figures
027.08450
Number of significant figures =
Rounded off to 5 significant figures =
MSD?
LSD?
7
27.084

## Slide 4: Chapter 3 - Number and Unit Formats
Identify any format errors in the following.
2 – 3 m/sec
42%
Body temperature, T, equals 98.6ºF.
1 x 10-4 J
One ft. equals 12 in. exactly.
25,233º
4E+4 ppm
2 m/s to 3 m/s
42 %
T 98.6 ºF
0.1 mJ
ft
25 233º
40 mL/L or 40 mg/g …

## Slide 5: Basic Electronics – R, C and L
Knowing R, C, L, V and I, determine
Potential difference across a resistor, capacitor and inductor
in series
IR + (1/C)∫I()d + LdI/dt
Current across a resistor, capacitor and inductor in parallel
V/R + CdV/dt + (1/L)∫V()d
Current related to charge
I = dq/dt
DC potential difference across 2 inductors in parallel
V = LTdI/dt = [(L1+L2)/L1L2]dI/dt = 0

## Slide 6: Chapter 4 – Wheatstone Bridge
Given R1, R2, R3, R4, Ei and Eo,
Derive the basic Wheatstone bridge equation
Eo = Ei [R1/(R1+R2)-R3/(R3+R4)]
What does this become when the bridge is balanced ?
R1/R2 = R3/R4
When all R’s are initially the same and the bridge is used
in the deflection mode ?
Eo = Ei [(R/R)/(4+2R/R)]
Voltage/force relation for same on a cantilever beam
Eo = Ei (R/R) = constant x F

## Slide 7: Chapter 4 – Miscellaneous
When measuring a voltage, the input impedance of the
voltmeter must be
much greater than the equivalent circuit’s output impedance
When measuring a current, the input impedance of the
ammeter must be
much less than the equivalent circuit’s output impedance
What is the resistance of a typical strain gage ?
O(100 )
What is the basic relation between R and T (temperature)
for a wire?
R = Ro[1+(T-To)]

## Slide 8: Chapter 5 - Calibration
What is the static sensitivity of the calibration curve
F = 250 W + 125 at W = 2 ?
dF/dW|W=2 = 250
What is the order of each of the following systems ?
Strain gage
Pressure Transducer
Accelerometer
RC circuit
Thermocouple
Pitot-static tube
zero
second
second
first
first
zero

## Slide 9: Chapter 5 – Dynamic Response
For a RC circuit (R = 2 ; C = 0.5 F) with step input forcing from 0 V to 1 V:
  What is the V of the circuit at 1 s ?
  What is the V of the circuit at 5 s ?
0.6321 V (0.6321V at  )
  What is the % dynamic error at 1 s ?
36.79 ( = 1 - M)
Now with sine input forcing of 3sin2t:
  What is its phase lag in degrees?
  What is its phase lag in s ?
  What is its magnitude ratio ?
-(180/)tan-1() = -63.43
0.55 s [ = tan-1(
0.448 [M = 1/√(1+ 
~1.0 V (>0.99V at 5 )

## Slide 10: First Order – Sine Input
 = 2
 = 2
 = -63.43
M = 0.448

## Slide 11: Chapter 5 – Dynamic Response
Is the RLC circuit (R = 2 ; C = 0.5 F; L = 0.5 H) underdamped, critically damped, or overdamped ?
 = R/√(4L/C) = 1 >> critically damped
With sine input forcing of 3sin2t:
  What is its magnitude ratio ?
n = √(1/LC)
= (2)(0.5) = 1
>>
M = 1/(2/n)
= 0.5 (see eqn [5.64])

## Slide 12: Chapter 5 – Some more ?s
What is M() at -6 dB ?
-6 dB = 20 log10 M() >> M()
or easier
-6 dB = 2 x -3 dB = 2 x 20 log10 1/√2
= 20 log10 (1/√2 )2 >> M() = 0.5

## Slide 13: Chapter 6 – Measurement Systems
A: What is the flow velocity if p = 58 Pa ?
U = √(2p/) = √[(2)(58)/1.16] = 10 m/s
A-B: If R = 100  and Rs = 200  at U = 0, Ei = 5.0 V,
what is Rx to have Eo = 0 V ?
This is the ‘balanced bridge’ condition
>> 1/100 = 1/Rs + 1/Rx >> Rx = 200

## Slide 14: Chapter 6 – Measurement Systems
A-B: At the highest U, the parallel combination of Rx and Rs
increases by 20 %. What is Eo ?
For this situation, Eo = Ei[(R/R)/(4+2R/R)]
= 5[0.2/(4+0.4)] = 0.23 V
B-C: What is the amplifier gain to achieve 80 % of the
full-scale range of the A/D board at the highest U ?
Assume a 0 V to 10 V A/D board >> G = (0.8)(10)/0.23 = 35
B-C: If a non-inverting opamp is used, what should be the
values of its resistances ?
G = 35 = Eo/Ei = 1 +R2/R1 >> R2/R1 = 34

## Slide 15: Chapter 6 – Measurement Systems
C-D: What type of filter would be appropriate to use ?
An anti-aliasing (low pass) filter with fcutoff = fN.
D-E: What bit A/D board is required to have less than 0.2 %
error in the voltage reading of the highest-U condition ?
At the highest-U condition, E = 8 V >> absolute quantization
error < (0.002)(8) = 0.016 V = 16 mV.
M = 8 >> error = 19.6 mV and M = 12 >> error = 1.22 mV
So, a 12-bit A/D board will suffice.

## Slide 16: Chapter 7 – Normal Probability
What is the probability that a student will score between 75 and 90 on an exam, assuming that the scores are distributed normally with a mean of 60 and a standard deviation of 15 ?
z75 = (75-60)/15 = 1 and z90 = (90-60)/15 = 2
one-sided z-table >>
P75 = 0.3413 and P90 = 0.4772
>> P75 to 90 = 0.4772 – 0.3413 = 0.1359

## Slide 17: Chapter 8 – Student-t Statistics
What is the probability that a student will score between 75 and 90 on an exam, assuming that the scores are based on 9 students, with a mean of 60 and a standard deviation of 15 ?
t75 = (75-60)/15 = 1 and t90 = (90-60)/15 = 2
two-sided t-table for  = 8 >>
P75 = 0.6534 and P90 = 0.9195 (Table 8.3)
>> P75 to 90 = [0.9195 – 0.6534]/2 = 0.1331

## Slide 18: Chapter 8 – Statistical Estimates
Given the mean and standard deviation are 10 and 1.5, respectively, for a sample of 16, estimate with 95 % confidence the ranges within which are the true mean and standard deviation.
range for true mean = sample mean ± t,PSx/√N
= 10 ± (2.131)(1.5)/√16 >> between 9.2 and 10.8
range for true variance: Sx2//22 ≤ 2 ≤ Sx2//22
>> (15)(1.5)2/27.5 ≤ 2 ≤ (15 )(1.5)2/6.26 for  = 0.05
>> 1.23 ≤ 2 ≤ 5.39
>> 1.11 ≤  ≤ 2.32

## Slide 19: Chapter 8 – 2 Statistics
The sample standard deviation of the length of 12 widgets taken off of an assembly lines is 0.20 mm. What must be the widget population’s standard deviation to support the conclusion that the probability is 50 % for any difference between the sample’s and population’s standard deviations to be the result of random effects ?
 ≡ Sx2/2 = 10.3 for  = 11
>> 2 = (11)(0.20)2/10.3 = 0.0427
>>  = 0.21 mm

## Slide 20: Chapter 9 – Uncertainty
A calibrated force balance is used to determine the lift coefficient of an airfoil. N force measurements are made under ‘fixed’ wind tunnel conditions. The output of the force balance is recorded by a computer. Identify and state how to quantify all the possible uncertainties.
calibration uL: ux-from-y (Fig. 10.9 and caleyIII.m)
temporal precision: uV-variation = t,PSV/√N (want average)
L to CL conversion: CL = L/(0.5U2) (result uncertainty,
which includes instrument uncertainties)
A/D quantization: Q/2 = EFSR/2M+1
convert uV’s to uL’s

## Slide 21: Chapter 9 – Uncertainty
How are all of these uncertainties combined to give the final estimate of CL?
CL = CLmean ± UCL = CLmean ± t,PuCL,
where uCL is the quadrature
combination of all the uL uncertainties
If r = xn, what is the fractional uncertainty in r ?
ur/|r| = |n| ux/|x|

## Slide 22: Chapter 10 – Regression
Can a least-squares linear regression analysis be used to determine the best fit of (F,V) data to the nonlinear expression V = k + bFc, where k is V when F = 0 ?
Yes - but how ?
Use V* = V – k >> V* = bFc.
Then take log10 of both sides of the expression
>> log10V* = log10b + clog10F
A LSLRA of log10V* versus log10F gives b and c.

## Slide 23: Chapter 10 – Regression
What regression parameter quantifies the quality of the best-fit?
The standard error of the fit, Syx

## Slide 24: Chapter 11 – Signal Characterization
A collection of time-history records is called an
When the ensemble-averaged values of a random signal equal the corresponding average values computed over time for an arbitrary, single time history in the ensemble, the signal is
ensemble.
ergodic.
When f(t) = f(t +T), the signal is and T denotes the signal’s
periodic
period.

## Slide 25: Chapter 11 – Signal Characterization
Given y(t) = Csin(nt+), what symbol and units denote
phase
 (radians)
amplitude
cyclic frequency
C (y units)
f (Hz)
Arrange in order of descending value:
mean, rms, standard deviation
All we know is that rms ≥ mean.
Know how to compute a Fourier series.

## Slide 26: Chapter 12 – Digital Signal Analysis
What must fs be to avoid aliasing ?
fs > 2 fmax
What must fs be to avoid amplitude ambiguity ?
fs = 1/t; Nt = Ts; Ts = mTfundamental
>> fs = N/(mTfundamental),
where Tfundamental contains all integer
multiples of each component’s period.

## Slide 27: Chapter 12 – Digital Signal Analysis
At what cyclic frequency will y(t) = 3sin(4t) appear if fs = 6 Hz?
2 Hz (f/fN = 2f/fs = 4/fs < 1 >> no aliasing)
fs = 4 Hz ?
fs = 2 Hz ?
2 Hz (f/fN = 2f/fs = 4/fs = 1)
0 Hz (f/fN = 2f/fs = 4/fs = 2 >> aliasing to 0fN)
fs = 1.5 Hz ?
0.5 Hz (f/fN = 2f/fs = 4/fs = 8/3
>> aliasing to 2fN/3 = fs/3 = 0.5)
Amplitude ambiguity occurs at what above fs’s ?
only at fs = 1.5 Hz